EE 458/533 – Power Electronics Controls
Homework 2
Due Date: Thursday January 20th 2021

Taking the derivative with respect to x1 and x2, the same values for A and B are found such that \dot{\hat{x}}(t) = A \hat{x}(t) +B \hat{u}(t) .

2. Given d=0.5, Gig(s) and Gvg(s) will have no response since they have terms of (2D-1).
  Half the switching frequency is 25kHz/2 = 12.5kHz, however the cross over frequencies occur at frequencies much greater than this.
  The system is stable due to large positive phase margin in Gid(s). Phase margin shows how much the system gain can be increased before it is unstable. There is also small positive phase margin in Gvd(s).
TF	GM (dB)	PM (deg)	WG (Hz)	WP (Hz)	Stability
Gid(s)	inf	90.01	nan	106,182	yes
Gig(s)	inf	inf	nan	nan	yes
Gvd(s)	inf	2.25	nan	41,180	yes
Gvg(s)	inf	inf	nan	nan	yes